## Slide 1: Ansible
Gopal Naganaboyina
Gurpreet Gill
February, 2019

## Slide 2: Agenda
Introduction
Networking Modules
Playbooks
Ansible Tower
Ansible Galaxy
Lab Demo
Reference

## Slide 3: Introduction

## Slide 4: Introduction
Objective
  Introduce Ansible
  Get a view of a typical automation system, so you can position DNAC appropriately
Methodology
  High level lecture
  Optional hands-on lab for closer look

## Slide 5: What is Ansible
Open-source automation platform
Efficient automation of:
  Software provisioning
  Configuration management
  Application deployment
Agentless
  Doesn’t need any agent running on the managed devices

## Slide 6: What is Ansible
Automation model: 2 components
  Ansible Control Machine: Linux server with Ansible SW
  Managed devices: Devices that are being automated by Ansible.
Ansible Control Machine talks to devices over SSH
  Supports other transports
Only requirement on network devices: enable SSH

## Slide 7: Common Files
Config file
Inventory file
Playbook file

## Slide 8: Ansible Concepts: Config File
File to tune Ansible environment
To find your Ansible config file, do:
  $ ansible --version
Other methods to customize:
  Multiple config files
  Environmental settings
  Command line options
  Roles

## Slide 9: Ansible Concepts: Inventory File
Managed device info is saved in inventory file
Device info can be listed as individual hosts or groups
Variables can be assigned to hosts or groups
Well-known group names:
  all
  ungrouped
Example:
$ cat /etc/ansible/hosts
[IOS]
172.16.101.91 ansible_user=cisco ansible_ssh_pass=cisco
[XR]
172.16.101.92 ansible_user=cisco ansible_ssh_pass=cisco
[ALL:children]
IOS
XR

## Slide 10: Ansible Concepts: Modules
Modules are the nuts and bolts of Ansible automation tasks
Playbooks use Modules to execute tasks on the managed devices
Modules are Operating System specific.
  ios_command
  junos_config
$ ansible IOS -m raw -a “show ip route sum”
$ cat ios_sh_ip_route_sum.yml
---
- name: route summary from IOS devices
hosts: IOS
gather_facts: false
tasks:
- raw: sho ip route summary

## Slide 11: Ansible Concepts: YAML
YAML is a data serialization language
YAML = YAML Ain't Markup Language
YAML is intuitive and human readable
Ansible playbooks are written in YAML

## Slide 12: Ansible Concepts: YAML
Key-value-pair is represented as:
  <key><colon><space><value>
List: “ordered data”, represented as:
  <dash><space><data>
Dictionary: “non-ordered data”
  Bunch of key-value pairs
There can be list of dictionaries and dictionary of lists
Key-value pair
  platform: ASR9K
List
  - show ip int brief
  - show ip route summ
Dictionary
  name: Verify Router OS
  hosts: IOS
  gather_facts: false
  connection: local

## Slide 13: Ansible Concepts: Playbooks
Playbooks are the main means of Ansible automation.
Playbook is a collection of plays
Each play is a collection tasks
Each task is a collection of modules
Example structure:
- name: play1
hosts: group1
tasks:
- module1: parameters
- module2: parameters
- name: play2
hosts: group2
tasks:
- module1: parameters
- module2: parameters

## Slide 14: Ansible Concepts: Playbooks
Playbooks are the main means of Ansible automation.
Playbook is a collection of plays
Each play is a collection tasks
Each task is a collection of modules
Example structure:
- name: play1
hosts: group1
tasks:
- module1: parameters
- module2: parameters
- name: play2
hosts: group2
tasks:
- module1: parameters
- module2: parameters

## Slide 15: Ansible Concepts: Playbooks
Playbooks are the main means of Ansible automation.
Playbook is a collection of plays
Each play is a collection tasks
Each task is a collection of modules
Example structure:
- name: play1
hosts: group1
tasks:
- module1: parameters
- module2: parameters
- name: play2
hosts: group2
tasks:
- module1: parameters
- module2: parameters
Target
Action

## Slide 16: Basic Playbooks

## Slide 17: Basic Playbooks: ios & xr command module
Module Names: ios_command & iosxr_command
Module sends exec command to remote devices and returns the results
Both modules require local connection execution method
Required Parameters for ios & xr command module:
    - commands option : specify router command to retrieve data

## Slide 18: ios_command
iosxr_command
---
- name: IOS Module Router Config
hosts: IOS
gather_facts: false
connection: local
tasks:
- name: Collect version info
ios_command:
commands:
- show version
register: ABC
- debug: var=ABC.stdout_lines
---
- name: XR Module Router Config
hosts: XR
gather_facts: false
connection: local
tasks:
- name: Collect version info
iosxr_command:
commands:
- show version
register: XYZ
- debug: var=XYZ.stdout_lines

## Slide 19: Basic Playbooks: Register & Debug
Register
  - The “register” statement is used to capture the output of a task into a variable.
  - In previous example, we are saving the output of the show commands to the variables, named ABC and XYZ.
  - Refer: http://docs.ansible.com/ansible/latest/playbooks_conditionals.html#register-variables
Debug
- The “debug” module prints statements during playbook execution.
- The ”debug” modules takes in a var parameter, which is the variable you want to print.
- Refer: http://docs.ansible.com/ansible/latest/debug_module.html

## Slide 20: Basic Playbooks: ios & xr config module
Module Names: ios_config & iosxr_config
The config modules are used to configure the cisco routers.
The modules uses parent and line options to structure the configuration in a hierarchical way.
Both modules require local connection execution method.

## Slide 21: ios_config
iosxr_config
---
- name: IOS Module Router Config
hosts: IOS
gather_facts: false
connection: local
tasks:
- name: Configure Interface Setting
ios_config:
parents: "interface Ethernet1”
lines:
- "description test”
- "ip address 172.31.1.1 255.255.255.0”
---
- name: XR Module Router Config
hosts: XR
gather_facts: false
connection: local
tasks:
- name: Configure Interface Setting
iosxr_config:
parents: "interface GigabitEthernet0/0/0/0”
lines:
- "description test”
- "ip address 172.31.1.1 255.255.255.0”

## Slide 22: Basic Playbooks: Variables
Ansible variables are used to store information that will change with each host.
Variable can be defined:
    inventory file (ansible_host), or
    created directly in the playbook, or
    created in a separate file and included within the playbook.
Variables are defined in playbooks
    Using“{{ }}” the single/double quotes around double curly brackets
    Using {{ }} the double curly brackets if its part of a sentence/string
---
- name: IOS Module Router Config
hosts: IOS
vars:
INTF: ethernet1
IP: 172.31.1.1
MASK: 255.255.255.252
tasks:
- name: Configure Interface Setting
ios_config:
parents: "interface {{INTF}}”
lines:
- "ip address {{IP}} {{MASK}}”

## Slide 23: Basic Playbooks: Loops
Ansible loops are used when performing a task repeatedly
Key words used: item, loop
tasks:
- name: Collect Rtr info
ios_command:
commands:
- show version
- show inventory
tasks:
- name: Collect Rtr info
ios_command:
commands: "{{ item }}"
loop:
- show version
- show inventory
Using Loop:

## Slide 24: Basic Playbooks: Conditionals
Ansible conditionals are used in a statement to decide whether to run the task or not.
Ansible uses a when clause to dictate a conditional which needs to be true in order for the task to be performed.
tasks:
- name: Collect Router Version
ios_command:
commands:
- show ip int bri
when: ansible_user == "cisco"

## Slide 25: Ansible Tower

## Slide 26: Ansible Tower
Commercial product by Red Hat
Targeted at mid/large enterprises
Web based, with GUI and visual dashboard
Handles large user base with varying skill levels
Features include:
  Role-based access control
  Job scheduling
  integrated notifications
  Graphical inventory management
  REST API and CLI

## Slide 28: Ansible Galaxy

## Slide 29: Ansible Galaxy
User community hub
Open source playbooks
Create, find, and share content with the community
Typical Linux style contribution

## Slide 31: Conclusion
Ansible is an open-source, agentless automation tool that can be leveraged for networks configuration management functions.
Ansible-playbooks provides capabilities to automate daily operations tasks.
Automating repetitive tasks with Ansible can reduce OPEX costs and improve efficiency.
With increasing support of modules, it is possible to automate even more network functions through Ansible.

## Slide 32: Network Automation- Lab Demo

## Slide 33: Lab topology and access info
Lab info
  VPN server
  Ansible controller
  R1 IOS router
  R2 XR router
LAB access
  Use Cisco-Anyconnect client to VPN-into the lab
  Type in lab VPN server IP address
  Click on settings-wheel and uncheck "block connections to untrusted servers

## Slide 34: Lab Guide
Ansible .cfg file
grep -v "#" /etc/ansible/ansible.cfg | grep -v ^$
[defaults]
inventory = /etc/ansible/hosts <14>
gathering = explicit <36>
host_key_checking = False <71>
timeout = 10 <103>
deprecation_warnings = False <180>
retry_files_enabled = False <257>
[inventory]
[privilege_escalation]
[paramiko_connection]
[ssh_connection]
[persistent_connection]
[accelerate]
[selinux]
[colors]
[diff]
[defaults]
[inventory]
[privilege_escalation]
[paramiko_connection]
[ssh_connection]
[persistent_connection]
[accelerate]
[selinux]
[colors]
[diff]

## Slide 35: Lab Guide
Host file
cat /etc/ansible/hosts
[IOS]
R1 ansible_host=172.16.101.XX ansible_user=cisco ansible_ssh_pass=cisco
[XR]
R2 ansible_host=172.16.101.XX ansible_user=cisco ansible_ssh_pass=cisco
[ALL:children]
IOS
XR

## Slide 36: Network Automation Exercises
Exercise 1 – Execute show commands with Ansible Playbook
    Create Ansible playbook to access router and execute show commands
    Use similar playbook and add verbose details of the show commands
Exercise 2 – Automatically backup router’s config to server daily
    Create Ansible playbook to capture router’s running config from all Cisco device types.
    Setup cron job to execute playbook daily and backup router’s config on server.
Exercise 3 – Create a playbook get device health check
    Create Ansible playbook to run health checks on devices
Exercise 4 – Ansible Vault
    Use ansible-vault feature to encrypt sensitive data in inventory files.

## Slide 37: Reference

## Slide 38: Reference
Ansbile user guide URL
Ansible installation URL
YAML resources
  http://docs.ansible.com/ansible/latest/YAMLSyntax.html
  http://www.yaml.org
  https://www.youtube.com/watch?v=cdLNKUoMc6c
  https://www.youtube.com/watch?v=U9_gfT0n_5Q
Ansible Training
  Ansible for the Absolute Beginner @Udemy Click here
  Ansible for Network Engineers @Udemy Click here
  Kirk Byers Ansible training Jive page
  Dcloud lab Ansible for Cisco Nexus Switches v1

## Slide 39: Acknowledgements

## Slide 40: Acknowledgements
Some material in this session are sourced from Ansible docs
  http://docs.ansible.com/ansible/latest/index.html

## Slide 41: Backup Slides

## Slide 42: Ansible Roles

## Slide 43: Playbook
Efficient Usage
---
- name: output from IOS routers
hosts: XR
gather_facts: false
connection: local
vars:
INTF: loopback1
tasks:
- name: read config
iosxr_command:
commands: show run int {{INTF}}
register: DATA
- name: print output
debug: var=DATA.stdout_lines
We can simplify
  Playbook of playbooks
We can modularize
  vars
  tasks
  And other components
We can reuse
  Modularize components that are used repeatedly

## Slide 44: Playbook of playbooks
We can call playbooks within a playbook
Playbook to acquire data from IOS and XR devices:
---
- name: ios config
import_playbook: basic_ios_cmd.yml
- name: xr config
import_playbook: basic_xr_cmd.yml

## Slide 45: Roles
Organize a large playbook into reusable file structures
Creates a separation of functions; variables, tasks, & templates in unique directories
Expects files main.yml, and .j2 files in respective folders
File structure can be created manually or automatically via ansible CLI – “ansible-galaxy”
[roles/
├── xr-ospf >> Name of this role
│ ├── defaults >> default variables for the role
│ │ └── main.yml
│ ├── files >> contains files which can be deployed
│ ├── handlers >> contains handlers
│ │ └── main.yml
│ ├── meta >> defines some meta data for this role
│ │ └── main.yml
│ ├── README.md
│ ├── tasks >> contains the list of tasks
│ │ └── main.yml
│ ├── templates >> contains templates which can be deployed
│ └── vars >> contains variables used in this role
Notes: Ansible directory structure is important in ansible especially with roles.
Galaxy, is a free site for searching, downloading, and sharing community developed roles. You can create your own roles and publish them on the ansible-galaxy website, allowing other users to download and use your role.

## Slide 46: Roles Style Config
---
- name: play-1-output from IOS routers
hosts: XR
gather_facts: false
connection: local
vars:
INTF: loopback1
tasks:
- name: read config
iosxr_command:
commands: show run int {{INTF}}
register: DATA
- name: print output
debug: var=DATA.stdout_lines
[roles/
├── xr-ospf >> Name of this role
│ ├── defaults >> default variables for the role
│ │ └── main.yml
│ ├── files >> contains files which can be deployed
│ ├── handlers >> contains handlers
│ │ └── main.yml
│ ├── meta >> defines some meta data for this role
│ │ └── main.yml
│ ├── README.md
│ ├── tasks >> contains the list of tasks
│ │ └── main.yml
│ ├── templates >> contains templates which can be deployed
│ └── vars >> contains variables used in this role

## Slide 47: Config Generation Using Templates
Templates contain common and device/role specific elements
Ansible uses Jinja 2 templating language for access to variables and logic/dynamic expression
Jinja 2 template files end with .j2 ext
Ansible can automatically access the Jinja2 templates through its Python API
Notes: when playbooks are run, variables are inserted into jinja2 templates, we get the configuration test as output
variables are global/regional variables are inserted into templates - Jina2 templates wrapped around variables/templates is ansible
Ansible removes/abstracts complexities from end user
jinja2 templates are python libraries and pytohon api

## Slide 48: Role with lists with single variables – Example 1
Creating a role to generate configuration across multiple devices
# Variable defined in xr-config/vars/main.yml
---
router_hostname:
- { hostname: router1 }
- { hostname: router2 }
- { hostname: router3 }
...
- name: execute xr-config role
hosts: localhost
gather_facts: no
roles:
- xr-config
# playbook for executing role of xr-config
# Executes main.yml in xr-config/tasks/main.yml
- name: Generate the configuration from templates
template: src=xr-config-template.j2 dest=/home/cisco/{{item.hostname}}.txt
with_items:
- "{{ router_hostname }}"
# tasks file for xr
# Leverages j2 template for standard and variable config
hostname {{item.hostname}}
service timestamps log datetime msec
service timestamps debug datetime msec
clock timezone {{item.timezone}} {{item.timezone_offset}}
clock summer-time {{item.timezone_dst}} recurring
Notes: Before we start using variables it’s important to know what are valid variable names. Variable names should be letters, numbers, and underscores. Variables should always start with a letter.You might have some templates for configuration files that are mostly the same, but slightly different based on those variables.Variables in Ansible are how we deal with differences between systems.

## Slide 49: Jinja2 Template – For loop
For Loop is a continuous loop until it runs out of inputs variables
For Loop is invoked using {% for x in y %} syntax and ends with {% endfor %} syntax
# /template/template.j2
{% for INTF in interface_list %}
interface {{INTF}}
cost 1
!
{% endfor %}
!
# /vars/main.yml
Interface_list:
- GigabitEthernet0/0/0/0
- GigabitEthernet0/0/0/1

## Slide 50: Hierarchical templates and Block configs
Base template *.J2 is pulled to specific template through {% extends ”base_config_template.j2" %} knob
Configurations from specific template are inserted through block configs that being with { % block x %} and end with { % endblock % }
## Config lines from lsr_config referring base template
{% extends "ler_lsr_config_template.j2" %}
#/templates/ lsr__config.j2
{% block rsvp %}
!
rsvp
{% for interface in interface_list_ler %}
interface {{interface}}
bandwidth percentage 100
!
{% endfor %}
{% endblock %}
#/templates/ ler_lsr_config_template.j2
hostname {{item.hostname}}
service timestamps log datetime msecservice timestamps debug datetime msectelnet vrf default ipv4 server max-servers 10telnet vrf Mgmt-intf ipv4 server max-servers 10domain name virl.infodomain lookup disablecdp
{% block rsvp %}
{% endblock %}
!,,